Winter Internship at LSI
Presentation
-Soumya V

---
TASKS TARGETTED
- Generate closed spaces by joining doors(openings).
- Store doors seperately with attributes.
- Generate polygons of the formed closed spaces.
- Generate centroids of the polygons.
- Give attributes to the centroids.
- Generate a network from the centroid points.
- Conversion to GML

---
GML File Regeneration
TASK:- Should be able to convert any input format to a standards complying GML file.
- Used ogr2ogr library with necessary flags.
- To cross check, reconverted to dxf,shp and opened with respective viewers.
- Proper GML file conversion is achieved, including the field titles and values.

---
Joining Doors-1
- Initial drawing:
  A room with a gap
  which is a door.
- Program detects points
  which are within a threshold
  distance of each other, and
  stores as doors.

---
Joining Doors-2
It then does two things:
1. Produces a layer with
all walls and the gap between the
walls closed, and the new line
has “Type” attribute value set to
“door”.

---
Joining Doors-3
2. Represents each door by its
centroid generating a seperate
layer for that.
- Each door-centroid is again
  associated with the following
  attributes:

---
Generating Polygons
- Now that we have a closed figure,
  a polygon is generated out of it.
- As we do this we also count the number of doors being included.
- The polygon detection algorithm joins all the lines having at least one common endpoint as of now, and can be extended to multiple rooms following a proper sequence.
- Works accurately only for single rooms as of now.

---
Centroid Generation
- Now that we have a polygon we can generate centroids, and also associate attributes with them:
- Each room-centroid also has a “Doors”
  attribute which stores the number of doors in the room.

---
Tackling Door-Detection
- Since detecting doors, using distances alone was causing many unforseen problems, an alternate dxf code was attempted.

---
WORK AHEAD-1
- Extending the existing polygon generation
  algorithm to work accuately for multiple rooms
  (with door detection).
- ISSUES Faced:
  - No in-built mechanisms, in any of the python libraries.
  - Lines are stored as an array in shp files, not in the order we see them, so moving clockwise or in a particular direction is difficult.
  - One hack is to sort on the basis of end-points,
    but that fails to address some cases.

---
WORK AHEAD-2
Discussion with Anurag:
The graph algorithm designed by him has the following prerequisites:
Every corridoor, or a path through which people can move through, is an edge.
- Doors opening into either other rooms or the corridors are nodes
- The points where edges cut each other, say corridor junctions will be nodes.

---
WORK AHEAD-3
Discussion with Anurag(contd):
So the final definitions are:
- NODE: Areas where people wait to evacuate/Areas where a waiting cluster transforms into a cluster in motion.
    ALL DOORS AND CORRIDOR JUNCTIONS
    - Associated attributes:Capacity.
- EDGE: Allows movement between nodes.
    ALL CORRIDORS, HALLWAYS AND STAIRWAYS.
    - Associated attributes:Length and Breadth

---
WORK AHEAD -4
Expected final Result:
A network on which the existing algorithm can be applied..

---
WORK AHEAD -5
- Can improve the door detection algorithm being used.
- Current one is based solely on distances and ranges.(Since the input is clean)
- May lead to unforseen errors.
- Extra doors may be detected.
- Raw data, where arcs represent doors, can be of greater use, but leads it to new complications.

---
Sources
- Research papers:
  - A “Door to Door” Path Finding Approach for Indoor Navigation.
    - L. Liu , S. Zlatanova
  - A Semantic model to Define Indoor Space in context of Emergency Evacuation.
    - Nishith Maheshwari , K. S. Rajan
- Google, Wikipedia.
- Py-ogrgdal-cookbook online.

---
THANK YOU